## Slide 1: Electronic Logs
How to blend them into your operation
Presented by:
Tom Deutsch, Integrated Loss Control, Inc.
January 21, 2016

## Slide 2: About this Webinar
This webinar has been developed to assist in providing you with the knowledge you will need to ensure fleet safety and compliance.
The information in this webinar is current as of the release date of the webinar, but information on policies, and government regulations may change over the course of time.
The information and rules outlined in this webinar are not intended to be comprehensive and additional information and requirements may apply.
Third party recording and presentation of this webinar is unauthorized.

## Slide 3: What is an electronic logging device (ELD)?
An ELD is technology that automatically records a driver’s driving time and other aspects of the hours-of-service (HOS) records. This allows easier, more accurate HOS recordkeeping. An ELD monitors a vehicle’s engine to capture data on whether the engine is running, whether the vehicle is moving, miles driven, and duration of engine operation (engine hours). ELD manufacturers must certify that ELDs meet technical standards in the ELD rule.

## Slide 4: Who must use an electronic logging device (ELD)? The ELD rule applies to motor carriers and drivers who are currently required to keep records of duty service (RODS) on paper or with an Automatic Onboard Recording Device (AOBRD) under the hours-of-service (HOS) regulations. Drivers who use the timecard exception, and don’t keep paper RODs, will not be required to use ELDs. The following drivers may keep paper RODS: Drivers who keep RODS no more than 8 days during any 30-day period. Driveaway-towaway drivers (transporting a vehicle for sale, lease, or repair), provided the vehicle driven is part of the shipment. Drivers of vehicles manufactured before model year 2000.

## Slide 5: What are the benefits of electronic logging devices (ELDs)?
ELDs make tracking hours-of-service (HOS) easier and more accurate. This helps prevent both deliberate and unintentional HOS violations and helps drivers avoid fines due to mistakes in paper logs. Improved compliance with HOS rules helps ensure drivers have time for adequate rest and to operate commercial vehicles safely. More accurate and consistent HOS records also facilitate enforcement and support carrier business operations, such as effective dispatching.

## Slide 6: What does engine synchronization mean for the purposes of electronic logging device (ELD) compliance?
In order to be compliant, an ELD must be able to directly monitor the vehicle’s engine operation to automatically capture engine power status (on or off), vehicle motion, miles driven, and engine hours.

## Slide 7: Can an electronic logging device (ELD) have a feature to warn drivers about approaching hours of service (HOS) limits?
Yes, the ELD rule allows, but does not require, warning or notification to drivers when they are nearing their HOS limits.

## Slide 8: Myths
No, the rule does not include requirements to control the vehicle or any other safety systems.
If a driver is running legally with paper logs, there should be no change in income.
No, however they will need to know how to transmit logs electronically to enforcement.
No,
Truck shuts off when driver runs out of hours.
Your drivers will make less money.
Drivers are forced to show DOT paper logs.
Drivers can change electronic logs.
Drivers can drive without logging.
Your entire fleet will quit by installing electronic logs.

## Slide 9: Some of the more common found ELD providers
People Net
OMI Trax
Fleetmatics
Rand McNally
JJ Keller

## Slide 10: What to look for when shopping for a system
Cost of equipment, monthly fees & installation
GPS capability
How it integrates with your network
Fuel Tax Reporting
Tracking Vehicles
Monitoring Vehicle Performance

## Slide 11: Who is responsible for certifying and registering electronic logging devices (ELDs)?
Manufacturers are responsible for certifying and registering their ELDs.

## Slide 12: What does the Electronic Logging Device (ELD) rule address?
The ELD rule:
•Requires ELD use by commercial drivers who are required to prepare hours-of-service (HOS) records of duty status (RODS).
•Sets ELD performance and design standards, and requires ELDs to be certified and registered with FMCSA.
•Establishes what supporting documents drivers and carriers are required to keep.
•Prohibits harassment of drivers based on ELD data or connected technology (such as fleet management system). The rule also provides recourse for drivers who believe they have been harassed.

## Slide 13: What exceptions are allowed by the Electronic Logging Device (ELD) rule?
Drivers who are not required to keep records of duty status (RODS) are not required to use ELDs. In addition, the following drivers are not required to use ELDs, but must maintain paper logs when required:
•Drivers who keep RODS no more than 8 days during any 30-day period.
•Driveaway-towaway drivers (transporting an empty vehicle for sale, lease, or repair), provided that the vehicle driven is part of the shipment.
•Drivers of vehicles manufactured before model year 2000.

## Slide 14: Can drivers operate commercial motor vehicles (CMVs) equipped with electronic logging devices (ELDs), if they are not required to use them due to an exception?
Yes. A motor carrier can configure an ELD to show an exception for a driver who is exempt from using an ELD. The carrier can also use the ELD notes (annotation) capability to record the driver’s exempt status.

## Slide 15: How soon can electronic logging devices (ELDs) be installed and used – and when must they be used in commercial motor vehicles (CMVs)?
Manufacturers can begin certifying and registering ELDs 60 days after the publication date of the rule (the “effective date”). Carriers or drivers can use registered ELDs as soon as they are available.
All motor carriers and drivers subject to the ELD rule must use either an ELD or an AOBRD (automatic onboard recording device) by the “compliance date” (two years from the publication date of the final ELD rule). Within four years after the publication date, all carriers and drivers subject to the rule must use only ELDs.

## Slide 16: How many supporting documents must be retained by motor carriers, and when must drivers submit them to the motor carrier?
Motor carriers must retain up to eight supporting documents for each 24-hour period that a driver is on-duty. Drivers must submit RODS and all their supporting documents to the motor carrier no later than 13 days after receiving them.

## Slide 17: What are the categories of supporting documents?
Given the diversity of the industry, FMCSA has identified five categories of supporting documents:
Bills of lading, itineraries, schedules, or equivalent documents that show the starting and ending location for each trip;
Dispatch records, trip records, or equivalent documents;
Expense receipts related to “on-duty/not driving” periods (meals, lodging, fuel, etc.);
Fleet management system communication records;
Payroll records, settlement sheets, or equivalent documents showing payment to a driver.
Drivers using paper RODS must also keep toll receipts – which do not count toward the eight-document cap.

## Slide 18: What information should be in the supporting documents?
Proposed: Supporting documents generally must include:
•Driver name (or a carrier-assigned identification number) on the document or on another document that allows the carrier to link the first document to the driver. The vehicle unit number may also be used, if that number can be linked to the driver.
•Date.
•Location (including the name of the nearest city, town, or village).
•Time.

## Slide 19: What must a motor carrier do with unassigned driving records from an electronic logging device (ELD)?
A motor carrier must review any unassigned records and either annotate them to explain why the time is unassigned, or assign them to the appropriate driver(s). If assigned to one or more drivers, each driver must re-certify the records if the assignment is correct. Carriers must retain unassigned driving records for at least six months, and make them available to safety officials.

## Slide 20: Can an ELD record be set to record minimum duty status durations, such as 15 minutes?
No, there is no minimum amount of time for ELD duty status recording. An ELD is more accurate, and records the actual time for each duty status entered.

## Slide 21: What information is automatically recorded by an electronic logging device (ELD)?
At regular intervals, ELDs automatically record date; time; location; engine hours; vehicle miles; and identification information for the vehicle, motor carrier, driver, and other users authorized by the motor carrier.

## Slide 22: When will an electronic logging device (ELD) automatically start to record a driving mode or status?
An ELD will switch to driving mode once the vehicle starts moving at a set speed threshold of no more than 5 miles per hour.

## Slide 23: When will an electronic logging device (ELD) automatically change the duty status from driving to the default duty status of on-duty not driving?
When the vehicle has not been in motion for five consecutive minutes, the ELD will prompt the driver to confirm driving status or enter the proper status. If the driver doesn’t respond within one minute, the ELD will switch to on-duty not driving status.

## Slide 24: If a driver is permitted to use a Commercial Motor Vehicle (CMV) for personal reasons, how must the driving time be recorded?
If a driver is relieved from all work responsibilities, time traveling between a driver’s home and terminal (or normal work reporting location) may be considered off-duty time. Traveling short distances from lodging (terminals or motels) to restaurants may also be considered off-duty time. However, a driver who uses a carrier’s vehicle for transportation home, and is later dispatched from home, would be considered on-duty from the time he/she leaves home. [Guidance Question 26 for 49 CFR 395.8]

## Slide 25: What does the electronic logging device (ELD) record when the personal conveyance status is selected and the commercial motor vehicle (CMV) is driven?
An ELD records all miles driven, regardless of status. However, when a driver is using a vehicle for authorized personal use (personal conveyance) the location is recorded only within an approximate 10-mile radius to protect driver privacy while off-duty.

## Slide 26: Can a logged-in co-driver make entries over his or her records using the electronic logging device (ELD) when he or she is not driving?
Yes, the driver who is not operating the vehicle may make entries over his or her own records when the vehicle is in motion. However, co-drivers cannot switch driving roles on the ELD when the vehicle is in motion.

## Slide 27: Who can edit an electronic logging device (ELD) record?
Both the driver and authorized carrier staff can make limited edits to an ELD record to correct mistakes or add missing information. All edits must include a note (annotation) to explain the reason for the edit. In addition, the driver must confirm (certify) that any carrier edit is accurate, and resubmit the records. If the driver chooses not to re-certify RODs, this is also reflected in the ELD record.
The ELD keeps the original, unedited record, along with the edits.
Example: a carrier edits a record to switch a period of time from “off-duty” to “on-duty not driving”, with a note that explains “Driver logged training time incorrectly as off-duty”. The edit and annotation are sent to the driver to verify. The edit is not accepted until the driver confirms it and resubmits the RODS.

## Slide 28: Can a user edit or change driving time that has been recorded by an electronic logging device (ELD) to non-driving time?
No, an ELD automatically records all of the time that a CMV is in motion as driving time that cannot be edited or changed to non-driving time.

## Slide 29: Are drivers allowed to edit their records of duty status (RODS) using the electronic logging device (ELD) back office support systems once they leave the commercial motor vehicle (CMV)?
Yes, a driver can make corrections or additions to ensure accurate RODS on an individual ELD or at the system level. The system will retain the original record, the edits, and the date, time, and identity of the individual who made the edits.

## Slide 30: What is the difference between an “edit” and an “annotation”?
An edit is a change to an ELD record to add missing information or correct a mistake. An annotation is a note to explain information in the record, or provide the reason for an update or edit. All edits must have notes (annotation), whether made by a driver or carrier.
For example, an edit showing time being switched from “off-duty” to “on-duty not driving” could be annotated by the carrier to note, “Driver logged training time incorrectly as off-duty.” This edit and annotation would then be sent to the driver for recertification.

## Slide 31: Who is responsible for the integrity of records of duty status in regards to the editing and certification rights of drivers and motor carriers?
The driver and the carrier share this responsibility. Driver certification is intended to help protect drivers from inaccurate carrier changes. However, if a driver is not available or willing to recertify a record, the carrier’s proposed edit and annotation will remain part of the record (along with the original, unedited record).

## Slide 32: Are the original electronic logging device (ELD) records retained after edits are made to them and available for drivers to access them?
Yes, each original record is kept, even after any edits and entries are made. A driver has the right to access the records for six months, either through the ELD, or another means of access that the carrier must provide.

## Slide 33: How can drivers access their records of duty status (RODS) from an electronic logging device (ELD)?
All ELDs will allow drivers to export data into a comma-delimited file (or CSV file) that can be used in Microsoft Excel, Word, notepad, and other common tools. Drivers can also access their records through the ELD display screen or a printout, depending on the ELD’s design.
If the RODS are no longer on the ELD in the vehicle, motor carriers must still make the data available for a period of six months. A carrier or driver might need to retrieve the records from a back-office system if they are not all available on the ELD.

## Slide 34: What procedure should be followed if multiple, compatible electronic logging devices (ELDs) are used to record a driver’s record of duty status (RODS) within a motor carrier’s operation?
The ELD in the vehicle the driver is currently operating must be able to produce a complete ELD report for that driver for the current 24-hour period and the previous 7 consecutive days.

## Slide 35: What procedure should be followed if an electronic logging device (ELD) is replaced or reset?
The driver must be able to provide safety officials data or documents for the current 24-hour period and the past 7 days in that vehicle, either as RODS loaded into the new or reset ELD or in paper format.

## Slide 36: What are the options for electronic logging devices (ELDs) to electronically transfer data?
An ELD must be able to either:
•Transmit data using wireless Web services and email, or
•Transfer data locally using a thumb or flash drive (USB2.0) or Bluetooth®.
A driver must also be able to provide either the display or a printout to an authorized safety official on request.

## Slide 37: Would a motor carrier be non-compliant with the ELD rule if the data cannot be sent electronically to an authorized safety official at roadside?
No, if electronic transfer is unavailable or not working, the driver can comply by showing the ELD display or a printout of the RODS.

## Slide 38: Is an ELD required to monitor its compliance with the ELD technical requirements?
Yes, an ELD must detect malfunctions and data problems due to power issues, data synchronization, missing data, timing, positioning, data recording, data transfer, and unidentified driver records.
The ELD will identify diagnostics and malfunctions, and display their status as “detected” or “cleared”. A driver can typically follow ELD instructions or carrier recommendations to resolve diagnostic events. A carrier must usually correct a malfunction.

## Slide 39: What must a driver do if there is an electronic logging device (ELD) malfunction?
If an ELD malfunctions, the driver must:
•Notify the carrier of the malfunction in writing within 24 hours;
•Create paper logs of RODS for the current 24-hour period and previous 7 days – unless the driver already has the records or retrieves them from the ELD; and
•Continue to prepare paper RODS until the ELD is repaired and compliant.

## Slide 40: What must a motor carrier do if there is an electronic logging device (ELD) malfunction?
If an ELD malfunctions, a motor carrier must either:
•Repair or replace the ELD within 8 days of a driver’s notification or carrier’s discovery of the malfunction, whichever comes first.
•Request an extension, if needed, by notifying the carrier’s State FMCSA Division Administrator within 5 days of the driver’s notification, providing:
◦Name, address, and telephone number of the carrier filing the request;
◦Make, model, and serial number of each ELD;
◦Date and location of each ELD malfunction as reported by the driver; and
◦Brief statement describing the carrier’s efforts to repair or replace the ELDs, including why the extension is needed.

## Slide 41: What is the definition of harassment in the Electronic Logging Device (ELD) rule?
Harassment is action taken by a motor carrier that the carrier knew (or should have known) would result in a driver violating the Hours of Service (HOS) rules or a situation where the driver is operating while ill or fatigued. The carrier’s action must be based on information from an ELD or other technology used in combination with an ELD. FMCSA explicitly prohibits a motor carrier from harassing a driver. [49 CFR 390.36]

## Slide 42: How do you implement them in your company?
Dispatch – They need to understand this will help with their day to day planning and gives them the ability to do long range planning. Each dispatcher will have access to each drivers log summary showing where the driver is with the 11,14, & 70 hour rule. ELD’s will require dispatchers to be better planners, and to utilize their fleet better.

## Slide 43: Implementation Continued
Drivers – will not make less income by having ELD’s. Most drivers with ELD’s make the same amount of money, unless currently, their company allows them to run extremely illegal with paper logs. Driver’s will need to plan their time differently which could affect their personal time. Most drivers that cheat when they don’t even need to.

## Slide 44: ELD Driver Training
Explain to each driver how the system works. A quick way a company can loose drivers is by giving an instruction sheet to the drivers and say figure it out.

## Slide 45: Drivers Need To Know
What to do if they forget to log off duty.
What will happen if the truck moves when driver is not logged on.
What to do when they run out of time on the road.
How to Personal Convey ( If the company allows PC )
How to plan their time.
How to send logs to enforcement.
How they will be audited against the ELD’s
When a driver needs to log off of the truck.
What information a driver is expected to input like trip number
trailer number etc.

## Slide 46: Company Settings
Most of the systems will have some automated settings. It is important the driver knows what the company settings are.
These settings are:
When will the system switch a driver to driving status
When will it switch to on duty not driving.

## Slide 47: Auditing ELD’s
A company should audit for Miles w/o Hours
PC abuse
½ hour break on line 1 or 2
On duty functions logged on line 4
Hourly violations
Combining on and off duty activities

## Slide 48: Questions?

## Slide 49: Thank you For Attending!